# Fuzzy controllers of  Mamdani and Takagi-Sugeno type

## Design of fuzzy controllers:

## Granulation (G)

## Fuzzification, (F)

## Inference, (I),

## Agregation, (A),

## Defuzzification  (D).

# F-I-A-D for controllers of Mamdani type

### Fuzzification:

In fuzzyfication stage there are formed membership functions for input variables. This operation is for condition of demonstration example illustrated in Fig.1. In case of deeper structuralization of premises, e.g.

Jesliže(((e(k) = A1)OR(e(k)=A2))AND(e(k)= B))  Pak (u(k) = C),

It is necessary to use a consistency  operator:

A(x10) = max  A1(x10), A2(x10).

Fig.1.:

# Inference

Recapitulation of  Madani  inference:

Mamdani fuzzy inference for value  x=x0 :

Let us have fuzzy sets  A, B defined on continuous universem universech X, Y.

Composition rule for Mamdani implication (computed for each y  Y, for

x=x0) the following form:

BM(y) = min A(x0 ), IMM(x0, y) = min A(x0 ), minA(x0), B(y).

Comparing quantities  A(x0) and  min A(x0), B(y) we have to consider three following cases :

(i)   (A(x0)  B(y))  (BM(y) = B(y)),

(ii)   (A(x0) ( B(y))  (BM(y) = A(x0)),

(iii)  (A(x0) = B(y))  (BM(y) = A(x0)).

Derived expressions for x=x0 and for all y  Y, and for the case of continuous universes X ( Y ( R1 ( R1 give very clear graphical construction for BM(y) - Fig.7.4.

Fig.7.4.

Example:

Let us consider two rules:

IF(((e(k) = A1)AND(e(k)= B1))  THEN (u(k) = C1),

IF(((e(k) = A2)AND(e(k)= B2))  THEN (u(k) = C2),

Input: e(k) = x10 , e(k) = x20.

Fig.:

Aggregation

As a result of “Inference” we obtain a few fuzzy sets that represent consequences of activated rules. Each of these rules “recommend” own fuzzy set of action variable.  Každé z těchto pravidel "doporučuje" jinou fuzzy množinu akční veličiny.

These fuzzy sets is necessary to combine to one (by operation Aggregation).

Aggregation is formed as union of fuzzy sets:

C(x10, x20) = C1(x10, x20)  C2(x10, x20),

Defuzzification

The goal of defuzzification is to transform a resulting fuzzy set C(x10, x20) into one real number (quantity of action variable).

There are a few methods:

- Centre of gravity of C(x10, x20):  u(k) = ( ((C(u) u du) / ( ((C(u)du).

- A generalized mean quantity: u(k) = (( (C(ui) ui) / (( (C(ui)) , pro i=1, …,n.

- Quantity that is assigned to a maximum value (C(ui).

Other methods are known as  “coa” (center of area), “mom” (mean of maxima).

# F-I-A-D for controllers of  Takagiho - Sugeno type

These controllers differs from Mamdani type in the right side of rules and in ways of “aggregation and defuzzification”. On the right side is not a fuzzy set but a real function.

Type of rules:

IF ((e(k) = A) AND (e(k) = B))   THEN (u(k) = f(e(k),e(k))),

e.g.:

IF ((e(k) = A) AND (e(k) = B)) THEN (u(k) = e(k) + 2 e(k))),

IF ((e(k) = A1)   THEN  (u(k) =  0.4 e(k))),

where  e(k), e(k), A, B, A1 have the same content and meaning as for Mamdani models and real functions in right sides are

f1(e(k),e(k)) = e(k) + 2 e(k)),

f2(e(k),e(k)) = 4 e(k) + 0 e(k)) .

Quantity of u(k) that represents activated rules is computed as a mean value

m             m

u = ( wi  ui)/ ( wi ) ,

1              1

where wi are “values of membership functions of ui(k)” computed for each rule. Number m is a number of rules. Quantities  wi are computed from values of membership function in left sides of rules.

For example in rules above for  e(k) = x10    e(k) = x20  we have:

w1 = min  A(x10 ), B(x20 ) , w2 = A1(x10 ).

Example: Let us consider Sugeno model with two rules and with fuzzy sets expressed in form of fuzzy numbers

A =  5.0, 6.0, 2.0, 1 , B =  0.5, 0.6, 0.2, 0.1 ,

A1 =  0.1, 3.0, 0, 1.0  .

Compute the value of action variable !

e(k) = 3.5  a  e(k) = 0.6.

A(3.5 ) = 0.25 , B(0.6 ) = 1.0, A1(3.5) =0.5,

w1 =min  0.25, 1.0  = 0.25.  , w2 = 0.5,

u1 = 3.5 + 2 * 0.6 = 4.7 , u2 = 0.4 * 3.5 = 1.4.

Resulting quantity of action variable:

u(k) = (0.25 * 4.7 + 0.5 * 1.4) / (0.25 + 0.5) = 2.5 .

Pozn.: Pokud jsme přijali výklad konceptů agregace a  defuzzifikace u regulátorů Mamdaniho typu, je vhodné poznamenat, že u Sugenovských modelů regulátorů  nedochází doslova k agregaci fuzzy množin (jak je jistě zřejmé), zejména proto, že výsledkem vyhodnocení každého pravidla je jednoprvková fuzzy množina hodnota u(k), hodnota funkce příslušnosti u(k).

Podobně speciální význam má postup defuzzifikace. Do výpočtu vstupují  jednoprvkové fuzzy množiny a  forma výpočtu má nejblíže k metodě zobecněné střední hodnoty.

2.4.2. Basic steps in design of fuzzy controllers

S1.:   Selection of the type of the controller.

S2.: Assignment of lingvistic variables to the selected systém variables (inputs, outputs, actions).

S3.  Determination of extents of fuzzy values and formation of profiles of fuzzy values.

S4.: The synthesis of rules of  the controller.

S5:  The selection of inference model.

S6.: The choise of aggregation procedure.

S7: The choise of the defuzzificarion methods.

Poznámka:

Postupně s prohlubováním teorie fuzzy regulátorů a s jejich aplikacemi se stále více ukazuje, že jde o velmi tvárné nelineární regulátory adaptovatelné k nejrůznějším řízeným systémům, spíše než o modifikace odvozené z univerzálních klasických regulátorů P, PI, PID, apod. Koncept "fuzzy regulátor" představuje tedy víceméně prostor pro syntézu  speciálního nelineárního regulátoru "na tělo" k řízenému systému.

Basic types of fuzzy controllers

Fuzzy  P-controller  :

IF (e(k) = A)   THEN (u(k) = B)

Fuzzy  PD - controller :

IF ((e(k) = A) AND (e(k) = B))   THEN  (u(k) = C)

Fuzzy  PI - controller :

IF ((e(k) = A) AND (e(k) = B))   THEN  (u(k) = C)

Fuzzy  PID - controller :

IF ((e(k)=A)AND(e(k)=B)AND(e(k)=C))  THEN (u(k)=D) ,

where  e(k) is a control error in k-th interval of sampling, e(k) is its first difference, e(k) is the second difference of  e(k), u(k)  is a action variable  and  u(k)  is its first difference. Symbols  A, B, C, D are lingvistic values (tj. fuzzy sets) of the correspponding lingvistic variables.

To je samozřejmě velmi hrubá klasifikace. Není tím řečeno, že všechna pravidla např. fuzzy PD regulátoru musí mít tvar (83.2). Jestliže např. jazyková proměnná regulační odchylky i jazyková proměnná její první diference byly granulovány do sedmi jazykových hodnot (Záporná velká, Záporná střední, Záporná nízká, Nula, Kladná nízká, Kladná střední a Kladná vysoká) je možno pro  fuzzy PD regulátor napsat základních 49 pravidel typu (83.2).

Výstupy fuzzy regulátorů PI a PID jsou diference hodnoty akční veličiny u(k) a jejich účinek je třeba "integrovat". U většině těchto fuzzy regulátorů se "integrace" realizuje "načítáním" přírůstků u(k). To je samozřejmě velmi hrubá aproximace.